## Slide 1
ISOE EG-SAM Interim Report
Chapter 7. Key Lessons Learned from Past Accidents
Report on behalf of the Sub Expert Group
Caroline SCHIEBER, Yoshihisa HAYASHIDA,
Rick DOTY
International Workshop on Occupational Radiation Protection in Severe Accident Management
17-18 June 2014

## Slide 2: Chapter Content
Key lessons learned from:
  TMI-2 accident (1979)
    Contribution from R. Doty
  Chernobyl accident (1986)
    Contribution from C. Schieber
  Fukushima accident (2011)
    Contribution from Y. Hayashida
Focus on occupational RP issues during emergency and recovery phases

## Slide 3: TMI-2 Accident (28 March 1979) (1)
Accident consequences
  45% of core melt, remaining in the reactor pressure vessel, which remained intact
Occupational tasks to be performed
  Starting just after the accident = “recovery phase”
  Objectives to decontaminate and defuel:
    Maintaining the reactor in a safe state
    Decontaminate the plant
    Process and immobilize fission products
    Remove and dispose reactor core

## Slide 4: TMI-2 Accident (28 March 1979) (2)
Total collective dose from March 1979 to December 1993 : About 66 person.Sv
Major Activities from 1986 to 1989 | Dose (person.Sv)
Defueling operations – reactor vessel | 6.98
Defueling support (tools, repairs, water clean-up) | 10.58
Reactor Building miscellaneous (robotics, crane operations, radioactive waste, etc.) | 7.65
Decontamination outside the Reactor Building | 4.24
Routine operations (ops, chemistry, RP) outside the Reactor Building | 2.77
Ex-vessel defueling (pressurizer, etc.) | 2.16
TOTAL | 34.38 (≈ 8 person.Sv/year)
23 July 1980
July 1984
1st reactor building entry
October 1985
Defueling began
Reactor vessel head removed
January 1990
Defueling completed
28 December 1993
Post Defueling Monitored Storage
Accident
28 March 1979

## Slide 5: TMI-2 Accident (28 March 1979) (3)
Some key lessons learned from ORP point of view
  Design changes/improvements:
    Remote monitoring of area radiation levels
    Collect and analyse of reactor coolant samples and other potentially highly radioactive samples without incurring unnecessary dose
    Airborne effluent monitoring systems to address the need for monitoring of higher concentrations of radioactive materials
  Training improvements:
    Emergency plan response training
    Conduct of drills and exercises
  Development of ‘unmanned robots’
    Characterization of source terms and/or clean-up of areas (highly contaminated/high radiation fields areas )

## Slide 6: Chernobyl Accident (26 April 1986) (1)
Accident consequences
  Explosion ruptured the reactor vessel – 10 days of fire
  High release of nuclear fuel (9% on NPP site; 44% on 80 km zone, 44% rest of USSR; 3% outside USSR)
Workers involved
  Urgent response team : 27th April 1986 – 20th May 1986
    35,000 persons (13,000 military - 22,000 civil)
  Recovery operation workers: 21st May 1986 – 30th November 1986
    89,000 persons (49,000 military – 40,000 civil)
  Total number of workers involved until 1990
    ≈ 600,000 persons (240,000 military servicemen)
Collective dose 1986 – 1990 :
  ≈ 60,000 person.Sv
    73% in 1986, 22% in 1987

## Slide 7: Chernobyl Accident (26 April 1986) (2)
1986 - 1990
1986
1987
1986 - 1988
Decontamination of reactor block, reactor site and roads
Radiation monitoring and security operations
Construction of Slavutich town
Construction of waste repositories
Construction of Sarcophagus
Construction of settlement for reactor personnel
Construction of water filtration system
RECOVERY OPERATIONS
FIRST ACTIONS
Fire control, Saving life, Cut-off ventilation / electricity, switching of cooling system, Examination of equipment, Radiation survey, and Water supply

## Slide 8: Chernobyl Accident (26 April 1986) (3)
Some key lessons learned from ORP point of view:
Monitoring /Dosimetry
  Need for adequate dose and dose rate measurement devices, able to cope with very high dose rates,
  Need for instrumental dosimetry of beta exposure,
  Necessity to create a centralised dose recording system,
Tools
  Develop robotics supporting high dose rates
  Develop suitable and adequate personal protective equipment
Training
  Not all emergency workers may be trained on RP (firemen, militaries, etc.)
Work management issue
  A very large number of recovery workers might be necessary

## Slide 9: Fukushima Accident (11 March 2011) (1)
Accident consequences
  Total loss of power supply
  Destruction of building, equipment installations, and other machineries
  Explosion and partial meltdown at plant facilities
  Large amount of radioactive release
Workers involved (on site)
  Immediately after tsunami: 400 workers (130 operators, 270 maintenance personnel)
  Emergency services: Fire-fighters, Police, Self-Defense Force
  Recovery workers: from March 2011 to March 2013: ≈ 33,000 workers (87% of contractors)

## Slide 10: Fukushima Accident (11 March 2011) (1)
Source : TEPCO Monthly publication – *Collective dose is estimated by multiplying the No of workers reported to be exposed by the average individual dose

## Slide 11: Fukushima Accident (11 March 2011) (3)
Some ORP issues (for emergency phase)
Monitoring / Dosimetry
  Unusable APD’s and dose reading devices
  Worker Dose Registration had to be performed manually
  Unusable WBC (shielding geometry and increase of background level)
  High number of persons to be controlled
Training
  Lack of training for workers involved in the emergency operations
Working conditions
  Major hazards: radiation, heat, stress, machine operation and manual handling
  Highly contaminated site by deposition of uncontrolled radioactive releases
  Increase of radiation levels on the entire site
  Very high number of workers needed

## Slide 12: Key topics & Discussion points
Major differences between the three accidents, however, from the point of view of ORP, some similarities in the issues, eg:
  Monitoring and recording of doses
  Tools/robotics adapted to high level of radiation conditions
  Adapted protective equipment (radiation, contamination, heat,..)
  Management of high number of workers
  Training (emergency workers, new workers employed for remediation, …)
Collection and analysis of feed back experience is essential to improve the preparedness of accident management:
  Need to understand much better how and when workers are exposed, as well as actions implemented to manage their protection